## Slide 1: More insight on Testbench
From Simple Verilog to Structured Verification

## Slide 2: Features
System task
File interaction
Applying stimulus at signal transition

## Slide 3: System task
A system task is a built-in command provided by the simulator, not synthesized into hardware.
They control or observe the simulation, but do not describe real hardware.
All system tasks start with a $ symbol (dollar sign) —
They are part of the simulation system, not the circuit.

## Slide 4: Most useful system tasks in Verilog TB

## Slide 15: Test Stimulus
Case-I: # delay & explicit signal value assignment for specific test cases
(Can we provide the stimulus for all possible test cases).
Case-II: # delay & signal value come from file (result may be stored in file)
Case-III: No # delay, but signal value (explicitly) would be changed before every positive edge
Case-IV: No # delay & signal value come from file & signal value (explicitly) would be changed before every positive edge

## Slide 18: Write a testbench for the 8-bit adder
“Apply the following input pairs to a and b at 0 ns, 10 ns, 20 ns, and 30 ns respectively:(5, 3), (10, 7), (100, 55), (255, 1).”

## Slide 19: Explicit time (delay) and the value of the signals

## Slide 22: Write a testbench for the 8-bit adder
Clk period = 10 ns
rst should be high initially till t=15 ns
Apply the following input pairs to a and b at 0 ns, 20 ns, 40 ns, and 60 ns respectively:(5, 3), (10, 7), (255, 1).”

## Slide 25: Four separate blocks: Each serving one specific purpose

## Slide 29: File-Based Testbench for Registered 8-bit Adder

## Slide 31: TestBench
Write a Verilog testbench for the registered 8-bit adder such that the inputs a and b are changed only at the negedge of the clock, ensuring the DUT samples them on the next posedge.

## Slide 35
We can automatically provide all possible input
stimuli for a and b

## Slide 40: Structured testbench

## Slide 41: Software framework  Structured TB

## Slide 42: Coding style
In plain (directed TB) Verilog, you write all of this in one file;
In structured/Layered TB approach, we split the code into separate blocks
  Classes
  Interface.
  They are reusable.

## Slide 43: SystemVerilog
Modular approach in TB: Reusable classes and interfaces.